## Slide 1
NoC Performance Analysis Tool with Hybrid Arbitration

## Slide 2: Agenda
Recap
New Modifications
Sample Results
Next Steps

## Slide 3
INHERITANCE
PRIMITIVE
(Base Class)
Queue
Injector
Sink
Arbiter
Priority Arbiter
RoundRobin
Arbiter
Split

## Slide 4
NETWORK OBTANED USING INPUT FILES
N1
N3
N2
N4
N5
N7
N6
N8
N9
Q1
PR1
RR1
Q3
Q4
Q2
Statistics.txt file
F1 = 0.2,9.2
F2=0.8,1.21
F3= 0.7,0.8
RR1= 2,0
PR1= 0.3,0
Q1=6,1
Q2=7,1
Q3=2,1
Q4=8,1
Network.txt
N1:F1,Q1
N2:F2,Q2
N3:Q1,RR1(N3;N4)
N4:Q2,RR1(N3;N4)
N5:RR1(N3;N4),Q4
N6:F3,Q3
N7:Q4,PR1(N7;N8)
N8:Q3,PR1(N7;N8)
N9:PR1(N7;N8),S1

## Slide 5
Statistics.txt
F1 = 0.2,9.2
F2=0.8,1.21
F3= 0.7,0.8
RR1= 2,0
PR1= 0.3,0
Q1=6,1
Q2=7,1
Q3=2,1
Q4=8,1
  Fn(injector)=Injection Rate, Squared coefficient of variation of inter arrival time
  Qn(Queue)=Buffer size, Type(FIFO)
  RRn or PRn (Arbiter) = Service time, Squared coefficient of variation of service time
READING STATISTICS.TXT FILE
Based on the field parts (F,Q,RR,PR) in the file corresponding primitive objects (injector,queue,...) are created by gving the suitable instances like buffersize for queue, injection rate for injector, etc.....

## Slide 6
  Each line is of format, Node: source Primitive, destination primitive
  Nodes are created, corresponding connections are made via pointers to the primitives.
  Primitive_map is a mapping from the name of the primitive to its pointer
READING NETWORK.TXT FILE
Network.txt
N1:F1,Q1
N2:F2,Q2
N3:Q1,RR1(N3;N4)
N4:Q2,RR1(N3;N4)
N5:RR1(N3;N4),Q4
N6:F3,Q3
N7:Q4,PR1(N7;N8)
N8:Q3,PR1(N7;N8)
N9:PR1(N7;N8),S1

## Slide 7
  WAITING TIME OF INJECTOR IS THE SUM OF WAITING TIMES OF QUEUES ENCOUNTERED IN ITS FLOW
  Maintain a map between the injector and the primitives encountered in its flow.
  If the encountered primitive is a queue, then push it to a vector mapped to the injector.
WAITING TIME CALCULATION

## Slide 8: Agenda
Recap
New Modifications
Sample Results
Next Steps

## Slide 9: Updates to Class Queue
New Data Members
  injection_rate: Represents the rate at which packets are injected into the queue.
  coeff_interarrival_time: Represents the coefficient used to calculate inter-arrival times between packets.
New Member Functions
  setInjectionRate(double &new_injection_rate):Sets the injection rate for the queue.
  setCoeffInterArrivalTime(double &new_coeff_interarrival_time) :Updates the coefficient for inter-arrival time calculation.
  setWaitingTime(double &new_waiting_time):Sets the waiting time for the queue.

## Slide 10: Updates to Class Node
New Data Members
  injection_rate
  coeff_interarrival_time
New Member Functions
  getInjectionRate()
  getCoeffInterArrivalTime()
  setInjectionRate(double &new_injection_rate)
  setCoeffInterArrivalTime(double &new_coeff_interarrival_time)

## Slide 11: Updates to Class Injector
New Data Members
  waiting_time: Represents the time Injector spend waiting before being processed.
New Member Functions
  getWaitingTime() :Retrieves the current waiting time for the injector.
  setWaitingTime(double &new_waiting_time) :Updates the waiting time for the injector.

## Slide 12: Agenda
Recap
New Modifications
Sample Results
Next Steps

## Slide 13: Configurations
RR(Round Robin) followed by PR(PRiority)
PR followed by RR

## Slide 14
N1:F1,Q1
N2:F2,Q2
N3:Q1,RR1
N4:Q2,RR1
N5:F3,Q3
N6:RR1,Q4
N7:Q3,PR1
N8:Q4,PR1
N9:PR1,Sink
Network.txt
F1=0.05,0.95
F2=0.05,0.95
F3=0.08,0.91
Q1=4,1
Q2=4,1
Q3=4,1
Q4=2,1
RR1=4.0,0.0
PR1=4.0,0.0
statistics.txt
Network Obtained using Input Files and it's Corresponding Output
Injector: F1 Waiting time: 4.94669
Injector: F2 Waiting time: 4.94669
Injector: F3 Waiting time: 1.27776
Queue: Q1 Waiting time: 1.1126
Queue: Q2 Waiting time: 1.1126
Queue: Q3 Waiting time: 1.27776
Queue: Q4 Waiting time: 3.83409
Queue Flow
F1: Q1,Q4
F2: Q2,Q4
F3: Q3
Output
Intermediate inputs
QUEUE | Inj.rate | Coeff | buffer
Q1 | 0.05 | 0.95 | 4
Q2 | 0.05 | 0.95 | 4
Q3 | 0.08 | 0.91 | 4
Q4 | 0.1 | 0.95 | 2
Input Files

## Slide 15
N1:F1,Q1
N2:F2,Q2
N3:Q1,PR1
N4:Q2,PR1
N5:F3,Q3
N6:PR1,Q4
N7:Q3,RR1
N8:Q4,RR1
N9:RR1,Sink
Network.txt
F1=0.05,0.95
F2=0.05,0.95
F3=0.08,0.91
Q1=4,1
Q2=4,1
Q3=4,1
Q4=2,1
RR1=4.0,0.0
PR1=4.0,0.0
statistics.txt
Network Obtained using Input Files and it's Corresponding Output
Injector: F1 Waiting time: 2.83394
Injector: F2 Waiting time: 3.66276
Injector: F3 Waiting time: 2.25662
Queue: Q1 Waiting time: 0.747892
Queue: Q2 Waiting time: 1.5767
Queue: Q3 Waiting time: 2.25662
Queue: Q4 Waiting time: 2.08605
Queue Flow
F1: Q1,Q4
F2: Q2,Q4
F3: Q3
Output
Intermediate inputs
QUEUE | Inj.rate | Coeff | buffer
Q1 | 0.05 | 0.95 | 4
Q2 | 0.05 | 0.95 | 4
Q3 | 0.08 | 0.91 | 4
Q4 | 0.1 | 0.95 | 2
Input Files

## Slide 16: Agenda
Recap
New Modifications
Sample Results
Next Steps

## Slide 17: Next Steps
Handling Complex Configurations:
  Implementing methods to track each flow till the sink, even in highly complex configurations.
Handling Finite Buffers:
  Updating the code to deal with cases where buffers have limited size and see how it affects performance.